## Slide 1: IMAGE DEBLURRING USING DEEP LEARNING
TEAM MEMBERS:
BHADRA MAYA ANILKUMAR
G PREETHI RAVISANKAR
GOURI A V
GOWRI H BHAGAVATHI
GUIDED BY:
Mr. ANOOP K JOHNSON
Dept. of ECE, MBCET
Dept of ECE, MBCET

## Slide 2: OBJECTIVE
PROBLEM STATEMENT : “Deblurring of blurry images from various camera footages with 70 –100 % accuracy.”
CAUSES :
Motion Blur: Blur due to movement of objects
Improper holding of the camera
Dirty lens
Wrong focusing
Depth of field
Image Deblurring Using Deep Learning
Dept of ECE, MBCET

## Slide 3: INTRODUCTION
Image Processing is a signal processing method in which input is an image and output is an enhanced image.
Image Deblurring is an image processing method that removes distortion from a blurry image.
Blurry images have long been a major problem in computer vision and image processing.
Applications in various fields like photography, medical imaging, forensic science, and astronomy.
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 4: BACKGROUND
Deep Learning: Subset of Machine Learning in AI that imitates the working of human brain.
DL has networks capable of learning unsupervised.
CNN: Capable of extracting features of input images through convolution using filters; weights are automatically learned during training.
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 5
A recurrent generative adversarial network is used to reconstruct high definition images.
A scale recurrent generator extracts spatio-temporal features and reconstruct sharp images in a coarse-to-fine form.
The discriminator takes blurry images as conditions, structural information of which assists in distinguishing real sharp images.
A progressive loss function is used to enhance the gradients in back propagation.
LITERATURE REVIEW- 1
J. Liu, W. Sun and M. Li, "Recurrent Conditional Generative Adversarial Network for Image Deblurring," in IEEE Access, vol. 7, pp. 6186-6193, 2019.
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 6
Wavelet transform is an effective denoising method related to regularized inversion.
It is utilized to decompose and extract the low- and high-frequency information of the blurred image, which is taken as the first step.
When the process highlights the approximate portion of the image feature, the blurry image will be smoothed so that the image is distorted.
Dept of ECE,MBCET
C. Min, G. Wen, B. Li and F. Fan, "Blind Deblurring via a Novel Recursive Deep CNN Improved by Wavelet Transform", IEEE Access, vol. 6, pp. 69242-69252, 2018.
LITERATURE REVIEW- 2
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 7
Contributions are in three fold:
Loss and architecture which obtain desirable results.
A method based on random trajectories for generating dataset.
A novel dataset and method for evaluation of algorithms based on how they improve object detection results.
O.Kupyn, V.Budzan, M.Mykhailych, D. Mishkin and J.Matas, "DeblurGAN: Blind Motion Deblurring Using Conditional Adversarial Networks,"IEEE/CVF, UT, 2018, pp.8183-8192.
LITERATURE REVIEW- 3
Image Deblurring Using Deep Learning
Dept of ECE, MBCET

## Slide 8
In this paper, a scale recurrent network has been proposed for the deblurring task.
Compared with deep multi-scale convolutional for dynamic scene deblurring; it has a simpler network structure, a smaller number of parameters and is easier to train.
Scale-Recurrent Network for Deep Image Deblurring Xin Tao, Hongyun Gao, Xiaoyong Shen, Jue Wang, Jiaya Jia; The IEEE CVPR, 2018, pp. 8174-8182.
LITERATURE REVIEW- 4
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 9: LITERATURE REVIEW- 5
A multi-scale convolutional neural network is proposed that restores sharp images in an end-to-end manner.
This method achieves the state-of-the-art performance in dynamic scene deblurring not only qualitatively, but also quantitatively.
S. Nah, T. H. Kim and K. M. Lee, "Deep Multi-scale Convolutional Neural Network for Dynamic Scene Deblurring," 2017 IEEE Conference on CVPR, Honolulu, HI, 2017, pp. 257-265.
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 10
Simultaneously addresses deblurring and super-resolution from blurred low resolution images.
Proves its superiority via experimenting both when the levels of blur are known and unknown ~ Deblurring Super-Resolution Convolutional Neural Network (DBSRCNN).
F. Albluwi, V. A. Krylov and R. Dahyot, "Image Deblurring and Super-Resolution Using Deep Convolutional Neural Networks," 2018 IEEE MLSP, Aalborg, 2018, pp. 1-6.
LITERATURE REVIEW- 6
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 11: GENERATIVE ADVERSIAL NETWORK (GAN)
Ability to preserve texture details in images.
Create solutions that are close to the real image and look perceptually convincing.
In Generative Adversial Network, two networks train against each other.
Generator misleads the discriminator by creating compelling fake inputs.
Discriminator tells if an input is real or artificial.
11
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 12
GAN
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 13: BASIC BLOCK DIAGRAM
Fig: Image Deblurring using GAN
BLURRY IMAGE
WRC-GAN
DEBLURRED IMAGE
Wavelet Recurrent Conditional GAN Network
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 14
SINGLE LEVEL 2D
DISCRETE WAVELET TRANSFORM
(HAAR)
HL
VL
DL
Image Deblurring Using Deep Learning
Dept of ECE, MBCET

## Slide 15
BASIC BLOCK DIAGRAM: WRC-GAN
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 16
BLOCK DIAGRAM: GENERATOR
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 17
BLOCK DIAGRAM: DISCRIMINATOR
Dept of ECE, MBCET
Image Deblurring Using Deep Learning
R(S)

## Slide 18
BLOCK DIAGRAM : WRC-GAN
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 19
DATASET
GOPRO
It blur images by integrating sharp images over time.
Generates blurred images through averaging adjacent short-exposure frames captured by a high-speed video camera.
This dataset can imitate the image blur type in natural scenes.
Images are captured from various scenes and are at a resolution of 1280 x 720.
The GoPro dataset consists of 2,103 image pairs for training & 11 sequences with 1, 111 image pairs for testing.
21
Image Deblurring Using Deep Learning
Dept of ECE, MBCET

## Slide 20
T
O
O
L
S
&
S
O
F
T
W
A
R
E
U
S
E
D
ANACONDA
TENSORFLOW
PYTHON
GRAPHICS PROCESSING UNIT
GPU
22
Image Deblurring Using Deep Learning
Dept of ECE, MBCET
KERAS

## Slide 21
TRAINING
WRC GAN- is trained for 4 epochs.
Learning rate polynomial decayed from 10^-4.
Expected training of minibatch size is set to 16.
Adam Optimizer is used with Hyper-parameters ꞵ1= 0.9,
ꞵ2 = 0.999, ɛ = 10^-8.
Implemented with Keras on TensorFlow framework in GPU.
23
Image Deblurring Using Deep Learning
Dept of ECE, MBCET

## Slide 22
PSNR
Peak Signal to Noise Ratio: It is the ratio of maximum possible power of original image to that of corrupting noise.
This measure is used to determine the restoration quality of the signal.
Large value of PSNR signifies better Restoration.
Major Feature: A minute spatial shift of an image leads to large numerical distortion but no visible distortion.
where R is the maximum fluctuation in the input image data type.
PERFORMANCE EVALUATION PARAMETER
Image Deblurring Using Deep Learning
Dept of ECE, MBCET

## Slide 23
PERFORMANCE EVALUATION PARAMETER (Contd.)
MSE
Mean Squared Error : It is the sum of the squared distances between the target variable and predicted values.
It is used to calculate the error by squaring the + or – errors with itself.
It is more accurate when compared to mean error computation.
MSE values ranges from 0 to ∞.
where M & N are rows and columns of the image.

## Slide 24: WORK PLAN
Dept of ECE,MBCET
SL NO. | MONTH PROJECT PHASE | AUG | SEP | OCT | NOV | DEC | JAN | FEB | MAR
1. | Problem Identification |  |  |  |  |  |  |  | 
2. | Literature Review |  |  |  |  |  |  |  | 
3. | Phase 1: Formulation of Methodology |  |  |  |  |  |  |  | 
4. | Phase 2: Setting up of GPU & Software |  |  |  |  |  |  |  | 
5. | Phase 3: Code Implementation |  |  |  |  |  |  |  | 
6. | Phase 4: Training and Testing |  |  |  |  |  |  |  | 
7. | Phase 5: Final Simulation and Demo |  |  |  |  |  |  |  | 
8. | Documentation of Project |  |  |  |  |  |  |  | 
Image Deblurring Using Deep Learning

## Slide 25
BUDGET!
Research works: Rs 500/-
Printing expenses: Rs 1500/-
Miscellaneous expenses: Rs 1000/-
Total expense: Rs 3000/-
Image Deblurring Using Deep Learning
Dept of ECE, MBCET

## Slide 26
OUTPUT

## Slide 27
OUTPUT

## Slide 28
WHAT’S NEXT ?
To include ConvLSTM blocks to the Generator network.
To train generator chained with discriminator.
To add discrete wavelet transform (DWT) to the model.
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 29: REFERENCES
[1] S. Nah, T. H. Kim and K. M. Lee, "Deep Multi-scale Convolutional Neural Network for Dynamic Scene Deblurring," 2017 IEEE Conference on Computer Vision and Pattern Recognition (CVPR), Honolulu, HI, 2017, pp. 257-265.
[2] C. Min, G. Wen, B. Li and F. Fan, "Blind Deblurring via a Novel Recursive Deep CNN Improved by Wavelet Transform", IEEE Access, vol. 6, pp. 69242-69252, 2018. Available: 10.1109/access.2018.2880279.
[3] Scale-Recurrent Network for Deep Image Deblurring Xin Tao, Hongyun Gao, Xiaoyong Shen, Jue Wang, Jiaya Jia; The IEEE Conference on Computer Vision and Pattern Recognition (CVPR), 2018, pp. 8174-8182.
[4] F. Albluwi, V. A. Krylov and R. Dahyot, "Image Deblurring and Super-Resolution Using Deep Convolutional Neural Networks," 2018 IEEE 28th International Workshop on Machine Learning for Signal Processing (MLSP), Aalborg, 2018, pp. 1-6.
[5] Jinshan Pan, Jiangxin Dong, Jimmy Ren, Liang Lin, Jinhui Tang, and Ming-Hsuan Yang, "Spatially Variant Linear Representation Models for Joint Filtering", IEEE Conference on Computer Vision and Pattern Recognition (CVPR), 2019.
Dept of ECE, MBCET
Image Deblurring Using Deep Learning

## Slide 30
THANK YOU…